## Slide 1: USING A DIGITAL VOLT- OHM - METER
Automotive Technology
Learning How Electricity Works

## Slide 2: What is Electricity?

## Slide 3: Electricity
Electricity is the flow of electrons along a conductor

## Slide 4: Voltage
Voltage is the force that pushes the electrons along a conductor.

## Slide 5: Amperage
Amperage is a measurement of the volume of electron flow.

## Slide 6: Ohms
Ohms is the measurement of resistance to the flow of electrons. This is the WORK that is being done. More Resistance = Less work Less Resistance = More work

## Slide 7
For instructional purposes electricity can be compared to water

## Slide 8: Direct Current Voltage
DC Volts V
All Batteries are DC, so this is the scale you will always use for batteries!

## Slide 9: Alternating Current Voltage
AC Volts V
~
Wall plugs are A/C, so this is the scale you will always use for wall plugs!

## Slide 10: Ohms
Ohms Ω
Used for measuring resistance in a circuit through a load or to find out if a part of the circuit is connected to another. Never when voltage is present!

## Slide 11: DC Voltage
DC voltage flows in only one direction.

## Slide 12: AC Voltage
AC voltage flows back and forth.

## Slide 13: VOM Leads
Inspect VOM leads and determine how to hook up to VOM.
BLACK LEAD → Common Ground (-)
RED LEAD → Ω Volts Hz (+)

## Slide 14: VOM Battery
Determine DVOM Battery Location
Inside back cover

## Slide 15: DVOM Scale
Always estimate what readings you anticipate getting and then set the meter to a value higher than what you are expecting to measure.

## Slide 16
Meters that do not have adjustable range settings are called auto-ranging.

## Slide 17: Automotive Use
What scale would you use to test the battery voltage of most cars?
20 V

## Slide 18: Continuity
To test the continuity or “connectedness” of a circuit, you should use what scale?
Ohms

## Slide 19: Continuity
You should never use which scale when the power is turned on or connected to the circuit?
Ohms

## Slide 20: Car Battery
Car batteries are for storing electricity, but they do not produce it.

## Slide 21: Draw Test
Milli-amp scales can be used for what test?
Draw Test

## Slide 22: Diode
A Diode is a one way check valve for electricity.

## Slide 23: Resistance
Define the following terms in relation to resistance (ohms):
Infinity = not connected
Open = not connected or “off”
Closed = connected or “on”
Shorted = Power to ground with no load

## Slide 24: OPEN CIRCUIT VOLTAGE CHART for 12 Volt Battery
According to the chart at left, the battery in this picture above is about 92% full

## Slide 25
DC Voltage |  |  |  |  |  |  |  |  |  |  | 
12.70 V |  |  |  |  |  |  |  |  |  |  | 
12.58 V |  |  |  |  |  |  |  |  |  |  | 
12.46 V |  |  |  |  |  |  |  |  |  |  | 
12.36 V |  |  |  |  |  |  |  |  |  |  | 
12.28 V |  |  |  |  |  |  |  |  |  |  | 
12.20 V |  |  |  |  |  |  |  |  |  |  | 
12.12 V |  |  |  |  |  |  |  |  |  |  | 
12.04 V |  |  |  |  |  |  |  |  |  |  | 
11.98 V |  |  |  |  |  |  |  |  |  |  | 
11.94V |  |  |  |  |  |  |  |  |  |  | 
11.90V |  |  |  |  |  |  |  |  |  |  | 
Percent Full | 0% | 10% | 20% | 30% | 40% | 50% | 60% | 70% | 80% | 90% | 100%
Note the correlation between voltage and percentage full

## Slide 26
Measure the Voltage of a D cell Battery
Use V Scale

## Slide 27
Measure the Voltage of a AA Battery
Use V Scale

## Slide 28
Measure the Voltage of a 9V Battery
Use V Scale (or 20V some meters)

## Slide 29
Measure the Voltage of a Button Battery
Use V Scale (or 20V some meters)

## Slide 30
Measure the Voltage of a Wall Plug Outlet
Use V˜ Scale (or 200V ˜ on some meters)

## Slide 31
Measure the Voltage of a 240V Outlet
Use V˜ (AC) Scale (or 700V ˜ on some meters)

## Slide 32: Questions?
Vance Bloom vbloom@hemetusd.org
Ed Kessel ekessel@hemetusd.org
Watch this Power Point again
2. Ask three other students
3. See 1 and 2 above…
4. Google it!